        USB To UART COMMUNICATION Using SiFive -HiFive1 Board

AIM:

        To establish an UART(Universal Asynchronous Receiver/Transmitter) Communication with USB interface between the Host Pc and Hifive1.

REQUIREMENTS:
- Hifive1 Microcontroller
- Usb cable(Type A Micro B)
- GTK term (Hyper Terminal program for Serial Communication)
- Eclipse IDE /gedit for C programing
- Gcc compiler on Host pc
- Freedom-e-SDK

NOTE:

- For Eclipse platform based IDE- use FREEDOM STUDIO / EMBEDDED STUDIO FOR RISC-V for built in Toolchains.
- JTAG(j-link) is Required to load the program.

PROCEDURE:

1.Set up the Host Pc environment for the Hifive1 application developement (Read getting started guide document of Hifive1 and user manual for Freedom e31) .

2.Understand the requirements for establishing the USB to UART communication.

3.Open IDE or gedit ,do codings and save it in a new seperate folder which should be in the Software directory of the freedom SDK.

4.If Coding is done through any text editors like 'gedit' a Makefile has to be created alongside .c file.

5.For code compilation,debugging read the manual of hifve1.

6.While using GTK term for serial I/O set the PORT=/dev/ttyUSB1 and Baud rate=115200, from the Configuration option.Enable the Local echo option aswell.

CODE FLOW:

  (Assuming that the code is going to be developed in gedit text editor)

STEP 1:
        Open gedit and save the program name with .c extension
STEP 2:
        Header files to be Included

- #include <stdint.h> // to specify exact-width integer types
- #include <string.h> // for string macros and funtions
- #include <stdio.h> // for standard input and output
- #include "platform.h" // for Hifive1 platform based funtions,macros and header files

STEP 3:
        Initialize UART

        CLOCK CONFIGURATION:

        HFROSC:- High frequency Ring Oscillator for High Speed Clock.
        Run off 16 MHz Crystal for accuracy

        // Make sure the HFROSC is on before the next line
        PRCI_REG(PRCI_HFROSCCFG) |= ROSC_EN(1); //enable ring oscillator configuration

        //Note that the first line is
        PRCI_REG(PRCI_PLLCFG) = (PLL_REFSEL(1) | PLL_BYPASS(1));
        PRCI_REG(PRCI_PLLCFG) |= (PLL_SEL(1));

        // Turn off HFROSC to save power
        PRCI_REG(PRCI_HFROSCCFG) &= ~(ROSC_EN(1));

Configure UART to print

        GPIO_REG(GPIO_OUTPUT_VAL) |= IOF0_UART0_MASK; //slelect the o/p gpio for uart
        GPIO_REG(GPIO_OUTPUT_EN) |= IOF0_UART0_MASK; //enable the o/p gpio pin
        GPIO_REG(GPIO_IOF_SEL) &= ~IOF0_UART0_MASK; // select the gpio uart pin
        GPIO_REG(GPIO_IOF_EN) |= IOF0_UART0_MASK; // enable the gpio uart pin

Set Baud Rate
UART0_REG(UART_REG_DIV) = <Value>;

        Assign enabled txdata nd rxdata to tx & rx control registers

UART0_REG(UART_REG_TXCTRL) = UART_TXEN;
UART0_REG(UART_REG_RXCTRL) = UART_RXEN;

Note: The Value for UART_REG_DIV could be either hard code eg-138(from Table of UART in Document) or using the formula { div = (input frq\ baud rate) -1 }
We can get the input clock frequencyfrom the get_clock_frequency() (refer init.c)

 Wait a bit to avoid corruption on the UART. (In some cases, switching to the IOF can lead to output glitches, so need to let the UART reciever time out and resynchronize to the real start of the stream.

        volatile int i=0;
        while(i < 10000){i++;}

STEP 4:
        Sample Functions to Tansmit and Receive data.

 static void _putc(char c) {
  while ((int32_t) UART0_REG(UART_REG_TXFIFO) < 0);
  UART0_REG(UART_REG_TXFIFO) = c;
}

int _getc(char * c){
  int32_t val = (int32_t) UART0_REG(UART_REG_RXFIFO);
  if (val > 0) {
    *c = val & 0xFF;
    return 1;
  }
  return 0;
}
static void _puts(const char * s) {
  while (*s != '\0'){
    _putc(*s++);
  }
}
We can also use read() and write() predefined funtions provided in the BSP
Directory- $freedom e sdk/bsp/libwrap/sys

Sample Program for USB-UART communication

        img-1

        img-2

        img-3

COMPILATION TERMINAL COMMAND

~/freedom-e-sdk$ make software PROGRAM=<program name> BOARD=freedom-e300-hifive1

UPLOAD TERMINAL COMMAND

~/freedom-e-sdk$ make upload PROGRAM=<program name> BOARD=freedom-e300-hifive1

Example :-maxvy02@maxvy02-OptiPlex-755:~/HIFIVE1/freedom-e-sdk$ make upload PROGRAM=USBcom BOARD=freedom-e300-hifive1

Note: For Debug-Refer Manuals (GDB & OPENOCD)

GTK TERM OUTPUT

      SIFIVE symbol print (no input has given) i/p-[HELLO WORLD]
        o/p-Echo:[HELLO WORLD]

GTK Term set up pictures
        click on gtkterm->configuration->Set port and Baud rate as shown below

   Enable local echo aswell

MAKEFILE

        Create a makefile for the program

sample:
TARGET = USBcom
C_SRCS += Usbcom.c
CFLAGS += -O2 -fno-builtin-printf -DNO_INIT

BSP_BASE = ../../bsp
include $(BSP_BASE)/env/common.mk

Additional INFO:

- This program was developed in Ubuntu 14.04 operating system.
- Go through schematics,Datasheet,user Manual of Hifive1 and E31 Risc-V processor
- Make use of github repository https://github.com/maxvytech/maxvytechRepo.git